METHOD FOR ENHANCEMENT OF POWER QUALITY AT POINT OF COMMON COUPLING OF WIND ENERGY SYSTEM

ABSTRACT

The  location  of  generation  facilities  for  wind  energy  is determined by wind energy resource availability, often far from high voltage (HV) power transmission grids and major consumption centers. In case of facilities with medium power  ratings,  the  WF  is  connected  through  medium  voltage  (MV)  distribution  headlines. A situation commonly found in such scheme is that the power generated is comparable to the transport power capacity of the power  grid to which the WF is connected, also known as weak grid connection. The main feature of this type of connections is the increased voltage regulation sensitivity to changes in load. So, the system’s ability to regulate voltage at the point of common  coupling  (PCC)  to  the  electrical  system  is  a key factor for the successful operation of the WF. Also, is well known that given the random nature of wind resources, the WF generates fluctuating electric power.

In this paper a compensation strategy based on a particular Custom Power System (CUPS) device, the Unified Power Quality Compensator (UPQC) has been proposed. A customized internal control scheme of the UPQC device was developed to regulate the voltage in the WF terminals, and to mitigate voltage fluctuations at grid side. The voltage regulation at WF terminal is conducted using the UPQC series converter, by voltage injection “in phase” with point of common coupling (PCC) voltage. On the other hand, the shunt converter is used to filter the WF generated power to prevent voltage fluctuations, requiring active and reactive power handling capability. The sharing of active power between converters is managed through the common DC link. Therefore the internal control strategy is based on the management of active and reactive power in the series and shunt converters of the UPQC, and the exchange of power between converters through UPQC DC–Link. This approach increases the compensation capability of the UPQC with respect to other custom strategies that use reactive power only.

The proposed compensation scheme enhances the system power quality, exploiting fully DC– bus energy storage and active power sharing between UPQC converters, features not present in DVR and D–STATCOM compensators. Simulations results show the effectiveness of the proposed compensation strategy for the enhancement of Power Quality and Wind Farm stability.

BLOCK DIAGRAM FOR PROPOSED SYSTEM

DESIGNG SOFTWARE AND TOOLS:

MAT LAB /SIMULATION Software and sim power systems tools are used. Mainly control system tools, power electronics and electrical elements tools are used.