A HYBRID AC/DC MICRO GRID AND ITS COORDINATION CONTROL

ABSTRACT

THREE PHASE ac power systems have existed for over 100 years due to their efficient transformation of ac power at different voltage levels and over long distance as well as the inherent characteristic from fossil energy driven rotating machines. Recently more renewable power conversion systems are connected in low voltage ac distribution systems as distributed generators or ac micro grids due to environmental issues caused by conventional fossil fueled power plants. Recently dc grids are resurging due to the development and deployment of renewable dc power sources and their inherent advantage for dc loads in commercial, industrial and residential applications, the dc micro grid has been proposed to integrate various distributed generators. However, ac sources have to be converted into dc before connected to a dc grid and dc/ac inverters are required for conventional ac loads.

This project proposes a hybrid ac/dc micro grid to reduce the processes of multiple dc–ac–dc or ac–dc–ac conversions in an individual ac or dc grid. The hybrid grid consists of both ac and dc networks connected together by multi-bidirectional converters. AC sources and loads are connected to the ac network whereas dc sources and loads are tied to the dc network. Energy storage systems can be connected to dc or ac links. The proposed hybrid grid can operate in a grid-tied or autonomous mode. The coordination control algorithms are proposed for smooth power transfer between ac and dc links and for stable system operation under various generation and load conditions. Uncertainty and intermittent characteristics of wind speed, solar irradiation level, ambient temperature, and load are also considered in system control and operation.

A small hybrid grid has been modeled and simulated using the Simulink in the MATLAB. The simulation results show that the system can maintain stable operation under the proposed coordination control schemes when the grid is switched from one operating condition to another.

Block diagram for proposed system

DESIGNING SOFTWARE AND TOOLS:

MAT LAB /SIMULATION Software and sim power systems tools are used. Mainly control system tools, power electronics and electrical elements tools are used.