AN IMPROVED MAXIMUM POWER POINT TRACKING FOR PHOTOVOLTAIC GRID-CONNECTED INVERTER BASED ON VOLTAGE-ORIENTED CONTROL

ABSTRACT

An improved maximum power point (MPP) tracking (MPPT) with better performance based on voltage-oriented control (VOC) is proposed to solve a fast changing irradiation problem. In VOC, a cascaded control structure with an outer dc link voltage control loop and an inner current control loop is used. The currents are controlled in a synchronous orthogonal d, q frame using a decoupled feedback control. The reference current of proportional–integral (PI) d-axis controller is extracted from the dc-side voltage regulator by applying the energy-balancing control. Furthermore, in order to achieve a unity power factor, the q-axis reference is set to zero.

The MPPT controller is applied to the reference of the outer loop control dc voltage photovoltaic (PV).Without PV array power measurement, the proposed MPPT identifies the correct direction of the MPP by processing the d-axis current reflecting the power grid side and the signal error of the PI outer loop designed to only represent the change in power due to the changing atmospheric conditions. The robust tracking capability under rapidly increasing and decreasing irradiance is verified experimentally with a PV array emulator.

In this project, the main component of the single-stage grid connected PV system is the three-phase voltage source inverter (VSI). Typically, simple inductors L are used as a filter interfacing inverter and mains. LCL filter provides advantages in costs and dynamics since smaller inductors can be used. However, in a grid-connected system, an LCL filter may cause resonance, which is a disaster for the system’s stability. Hence, control systems involving LCL filters are inevitably more complicated. The voltage-oriented control (VOC) method used for VSI employs an outer dc link voltage control loop and an inner current control loop to achieve fast dynamic response. The performance of the power flow depends largely on the quality of the applied current control strategy. In this project, the current control has been implemented in a rotating synchronous reference frame d, q because the controller can eliminate a steady-state error and has fast transient response by decoupling control.

Simulations and experimental results demonstrate that the proposed method provides effective, fast, and perfect tracking.

In this paper, the main component of the single-stage grid connected PV system is the three-phase voltage source inverter (VSI). Typically, simple inductors L are used as a filter interfacing inverter and mains, LCL filter provides advantages in costs and dynamics since smaller inductors can be used. However, in a grid-connected system, an LCL filter may cause resonance, which is a disaster for the system’s stability. Hence, control systems involving LCL filters are inevitably more complicated. The voltage-oriented control (VOC) method used for VSI employs an outer dc link voltage control loop and an inner current control loop to achieve fast dynamic response. The performance of the power flow depends largely on the quality of the applied current control strategy. In this paper, the current control has been implemented in a rotating synchronous reference frame d, q because the controller can eliminate a steady-state error and has fast transient response by decoupling control.

Block diagram for proposed system

DESIGNING SOFTWARE AND TOOLS:

MAT LAB /SIMULATION Software and sim power systems tools are used. Mainly control system tools, power electronics and electrical elements tools are used.