INDUCTION MOTOR DRIVE USING SEVEN LEVEL MULTILEVEL INVERTER FOR ENERGY SAVING IN VARIABLE TORQUE LOAD APPLICATION

ABSTRACT

The main objective of this project is to control the speed of an induction motor by using seven level diode clamped multilevel inverter to obtain high quality sinusoidal output voltage with reduced harmonics. The proposed Scheme for diode clamped multilevel inverter is multicarrier SPWM control. An open loop speed control can be achieved by using V/ƒ method. This method can be implemented by changing the supply voltage and frequency applied to the three phase induction motor at constant ratio. The proposed system is an effective replacement for the conventional method which has high switching losses, as a result a poor drive performance. The simulation result portrays the effective control in the motor speed and an enhanced drive performance through reduction in total harmonic distortion (THD). The effectiveness of the system is verified through simulation using simulink package.

In this project, a three-phase diode clamped multilevel inverter fed induction motor is described. The diode clamped inverter provides multiple voltage levels from a five level unidirectional voltage balancing method of diode clamped inverter. The voltage across the switches has only half of the dc bus voltage. These features effectively double the power rating of voltage source inverter for a given semiconductor device. The proposed inverter can reduce the harmonic contents by using multicarrier SPWM technique. It generates motor currents of high quality. V/ƒ is an efficient method for speed control in open loop. In this scheme, the speed of induction machine is controlled by the adjustable magnitude of stator voltages and its frequency in such a way that the air gap flux is always maintained at the desired value at the steady state. Here the speed of an induction motor is precisely controlled by using seven level diode clamped multilevel inverter.

BLOCK DIAGRAM:

DESIGNG SOFTWARE AND TOOLS:

MATLAB /SIMULATION Software and Sim Power Systems tools are used. Mainly control system tools, power electronics and electrical elements tools are used.