A Dstatcom-Control Scheme For Power Quality Improvement Of Grid Connected Wind Energy System For Balanced And Unbalanced Non Linear Loads

ABSTRACT

One of the main problems in wind energy generation is the connection to the grid. Injection of wind power into the grid affects the power quality resulting in poor performance of the system. The wind energy system faces frequently fluctuating voltage due to the nature of wind and introduction of harmonics into the system. The influence of the wind turbine in the grid system concerning the power quality measurements are-the active power, reactive power, variation of voltage, flicker, harmonics, and electrical behavior of switching operation and these are measured according to national/international guidelines specified in International Electro-technical Commission standard, IEC-61400.

The paper study demonstrates the power quality problem due to installation of wind turbine with the grid. In this proposed scheme distribution static compensator (DSTATCOM) is connected with a battery energy storage system (BESS) to mitigate the power quality issues. The battery energy storage is integrated to sustain the real power source under fluctuating wind power.

The DSTATCOM control scheme for the grid connected wind energy generation system for power quality improvement is simulated using MATLAB/SIMULINK in power system block set. Finally the proposed scheme is applied for both balanced and unbalanced nonlinear loads.

In this paper, an indirect current control technique (Singh et al., 2000a, b) is employed to obtain
gating signals for the Insulated Gate Bipolar Transistor (IGBT) devices used in current controlled voltage source inverter (CC-VSI) working as a DSTATCOM. A model of
DSTATCOM is developed using MATLAB for investigating the transient analysis of distribution system under balanced/unbalanced linear and non-linear threephase and single-phase loads (diode rectifier with R and RC load).

Block diagram for proposed system

DESIGNG SOFTWARE AND TOOLS:

MAT LAB /SIMULATION Software and sim power systems tools are used. Mainly control system tools, power electronics and electrical elements tools are used.