POWER FAILURE IN INDUSTRIES

AIM:

The main aim of this project is to identify the power failure in industries and domestic purpose.

PURPOSE:

The purpose of the project is to identify the power failure in industries and domestic purpose.

BLOCK DIAGRAM:-

Power Supply:

DESCRIPTION:

Now a day's every system is automated in order to face new challenges. In the present days Automated systems have less manual operations, flexibility, reliability and accurate. Due to this demand every field prefers automated control systems. Especially in the field of electronics, automated systems are giving great performance.

In this project we are identifying the power failure in industries and domestic purpose. In this project we are using two bulbs as loads these bulbs will be continuously on when there is supply. We are using current sensor and voltage sensor to sense current and voltage consumed by loads and ADC is to convert analog signal into digital. That converted data is given to microcontroller. If supply is not there or power failure then it is indicated by using led and the bulbs will not on.

This project uses regulated 5V, 500Ma power supply, 7805 three terminal voltage regulator is used for voltage regulation. Bridge type full wave rectifier is used to rectify the ac output of secondary of 230/12V step down transformer.

HARDWARE COMPONENTS:

- Micro controller

- Power supply

- LCD

- Relay

- Current Sensor

- Bulbs

- ADC

SOFTWARE TOOLS:

- Keil u-Vision

- Embedded ‘C’

- Express PCB

APPLICATIONS:

- Used in Industrial applications.

- Used in Home applications.

RESULT:

Hence, the power failure in industries and domestic purpose is implemented.

# Text boxes

ADC

RELAY

LCD

VOLTAGE

SENSOR

Regulator         section

Filter

Circuit

Bridge

Rectifier

Step Down

Transformer

MICRO
CONTROLER

TRANSFORMER

POWER SUPPLY`

CURRENT SENSOR

BUZZER

LOAD