AUTOMATIC SHOPPING MALLS DEVICES CONTROL

AIM:

The main aim of the project is visitors count based power management system for home/office and commercial buildings.

PURPOSE:

The purpose of the project is provides a system for saving power of a home/office

BLOCK DIAGRAM:

Power Supply:

DESCRIPTION:

The project Automatic power saving system for a home/office/shopping mall with security system is a method for automatic control of devices (lights, fans, or AC s) throughout home or in a shopping mall. A unique architecture of occupancy sensors include entry/exit sensors for detecting movement through doorways that separate rooms in the home, room motion sensors for detecting room occupancy, spot sensors to detect occupancy of specific locations within the rooms, and house status sensors to detect the status of certain parameters of the home. A central embedded controller communicates with the sensors and controlled objects over a communication network, where the sensors and controlled objects can be added to the system in a `plug and play` manner.

The present project provides a system for saving power of a home/office/shopping mall. This project is designed around a microcontroller which forms the control unit of the project.

According to this project, the no. of visitors entering into and exiting from the shopping mall is calculated and is displayed. Apart from this, the appliances are made ON and OFF according to the no. of persons present in the shopping mall by which power can be utilized with great efficiency. This is realized using IR sensors.

This project finds its place in places where the things wanted to done automatically with utilization of power in efficient and effective manner.

HARDWARE:

- Microcontroller

- LCD

- IR sensors

- Appliances

- Power supply

SOFTWARE:

- Keil

- Express PCB

- Express schematic

- Embedded ‘C’

APPLICATION:

- Implemented in shopping mall, industries and in home

RESULT:

By using this we can implement visitors count based power management system for home/office/shopping malls.

# Text boxes

IR

SENSORS (exit)

APPLIANCES

IR SENSORS (entry)

LCD

POWER SUPPLY

MICRO

CONTROLLER

Regulator         section

Filter

Circuit

Bridge

Rectifier

Step Down

Transformer